History of Weather Modification
Skew-T Lop P Diagrams

---
Upper Air Observations
Most Operational Soundings Are Made By Radiosondes

---
Radiosondes Measurements
Temperature
Relative Humidity
Wind Direction
and Speed
Pressure
Height

---
Radiosonde Data is Plotted on Charts
Manual Analysis has Plotting Done by Hand
Computational Analysis Performed Graphically

---
Computer Analysis of Radiosonde Data
Plotting and analysis is done by computer software.
Information is coded from tansmission/stored data.
Mandatory Levels
Significant Levels
Significant change in observed properties.

---
Skew T Log p Diagram
Coordinates
Pressure Decreases Logarithmically
Temperature Skewed @ 45° Angle
Easier to Identify Stable Layers

---
Pressure
200
300
400
500
600
700
800
900
1000
Pressure (mb)

---
Temperature
Pressure (mb)
1000
900
800
700
600
500
300
200
400
Temperature (oC)
30
40
20
10
0
-10
-20
-30
-40
-50
-60

---
Dry Adiabats
Dry Adiabatic Lapse Rate
Also Constant Potential Temperature

---
Dry Adiabats
200
117
107
300
97
87
400
500
77
600
67
700
57
800
900
-23
-13
-3
7
17
27
37
47
1000
Pressure (mb)
Temperature (oC)
30
40
20
10
0
-10
-20
-30
-40
-50
-60

---
Pseudoadiabats
Lines of constant saturated adiabatic lapse rate.
For saturated processes.

---
Pseudoadiabats
Temperature (oC)
Pressure (mb)
1000
900
800
700
600
500
300
200
400
30
40
20
10
0
-10
-20
-30
-40
-50
-60
2
5
9
14
17
22
25
30

---
Equivalent Potential Temperature (θe)
The potential temperature a parcel of air would have if all of its water vapor were condensed and the latent heat released warmed only the dry air.
A measure of the total energy of a parcel of air.
Conserved (or constant) for saturated adiabatic processes.
Pseudoadiabats are also lines of constant Equivalent Potential Temperature (θe)

---
Mixing Ratio
Conserved (or constant) for dry adiabatic ascent.
mv
mv

---
Mixing Ratio
.4
1
2
3
5
8
12
16
20
Pressure (mb)
1000
900
800
700
600
500
300
200
400
Temperature (oC)
30
40
20
10
0
-10
-20
-30
-40
-50
-60

---
Dew Point Temp.
Pressure (mb)
1000
900
800
700
600
500
300
200
400
Temperature (oC)
30
40
20
10
0
-10
-20
-30
-40
-50
-60