Atmospheric Chemistry - Simple Models
Casas Del Bosque winery in Casablanca valley Chile on September 26, 2013.

---
Models
The atmospheric evolution of a species X is given by the continuity equation:
{partial [X]} over {partial t}
nabla
Deposition
Emission
Transport
(Flux Divergence;
U is wind Vector)
Chemical Production and Loss
(Depends on concentrations
of other species)
Local Change in Concentration
with Time
Continuity equation cannot be solved exactly; hence, need to construct model (simplified representation.
Improve Model, Characterize its Error
Design Observational System to Test Model
Design Model; Make Assumptions needed
to Simplify Equations and Make them Solvable
Define Problem of Interest
Evaluate Model with Observations
Observations
Apply Model:
Make Hypotheses, Predictions
Courtesy of
Daniel J. Jacob

---
One-Box
What can
“box”
represent?
One-Box Model
Chemical
Production
Chemical
Loss
Processes that Control
Concentration X
L
X
P
Inflow Fin
Outflow Fout
D
E
In atmospheric “box” models is the spatial distribution of X resolved?
What are two
type of
deposition?
Emission
Deposition
Lifetimes Add in Parallel:
Courtesy of
Daniel J. Jacob
Loss Rate Constants Add in Series:

---
UAS
Well Mixed
 Atmosphere
Measurements made 19 September 2011 (10:35-11:00 local time) at Camp Grafton South using the Telemaster Unmanned Aircraft System's Meteorological Package.
What height could you use for the vertical extent of a box model?
Aerosol Counts [0.30 – 0.46 µm]
Altitude [m]

---
Balloon
Laramie Wyoming Balloon Measurement
Delene, D. J. and T. Deshler, Calibration of a Photometric Cloud Condensation Nucleus Counter Designed for Deployment on a Balloon Package, Journal of Atmospheric and Oceanic Technology, 17, 459-467, 2000.
IPCC [2001]

---
EXAMPLE: GLOBAL BOX MODEL FOR CO2 (Pg C yr-1)
Example: Global Box Model for CO2 (Pg C yr-1)
EXAMPLE: GLOBAL BOX MODEL FOR CO2 (Pg C yr-1)
	1980s	1990s
Atmospheric Increase	3.3 ± 0.1	3.2 3.3 ± 0.1
Emissions (Fossil Fuel, Cement)	5.4 ± 0.3	6.3 ± 0.4
Ocean-atmosphere Flux	-1.9 ± 0.6	-1.7 ± 0.5
Land-atmosphere Flux	-0.2 ± 0.7	-1.4 ± 0.7
Land-use Change	1.7 (0.6 to 2.5)	NA
Residual Terrestrial Sink	-1.9 (-3.8 to 0.3)	NA
Global CO2budgets (in PgC/yr) based on intra-decadal trends in atmospheric CO2and O2. Positive values are fluxes to the atmosphere;negative values represent uptake from the atmosphere. The fossil fuel emissions term for the 1980s (Marland et al., 2000) has been slightly revised downward since the SAR. Error bars denote uncertainty (±1σ), not interannual variability, which is substantially greater.
IPCC [2001]
Source: IPCC [2001], Chapter 3 – The Carbon Cycle and Atmospheric Carbon Dioxide

---
Constant Source
Species with Constant Source, 1st Order Sink
What does 1st order mean?
τ – Life or Residence Time, k - Rate Constant, S - Source Rate
Steady State Solution (dm/dt = 0)
If S and k are constant over t >> ,
then dm/dt goes to 0 and
m goes to S/k: quasi steady state
Initial Condition m(0)
What is less, half life
or e-folding time?
Characteristic Time  = 1/k for
Reaching Steady State
Decay of Initial Condition
Courtesy of Daniel J. Jacob
[Speaker Notes: First order means they are proportional to the mass inside the box. E-folding (mean lifetime or lifetime) is the time interval in which an exponentially growing quantity increases by a factor of e, it is the base-e analog of doubling time. Half-life is the time required for a quantity to reduce to half of the initial value. Lifetime is equal to half-life divided by the natural log of 2 Lifetime = 1.44 * half-life hence half life is less.]

---
Two-Box
Two-box Model
F12
m2
m1
F21
Mass Balance Equations:
(similar equation for dm2/dt)
If mass exchange between boxes is first-order:
Therefore, system of two coupled ODEs (or algebraic equations if system is assumed to be at steady state)
Courtesy of
Daniel J. Jacob

---
CO2
Latitudinal Gradient of CO2
LATITUDINAL GRADIENT OF CO2 , 1998-2009
Sine of Latitude
Courtesy of Peter Tans, NOAA
Observed latitudinal gradients of CO2 and δ13 C at CMDL sites located in the marine boundary layer. The δ13 C scale is plotted upside down. Long time scale of interhemispheric exchange can use 2-box model to place constraints on CO2 sources/sinks in each hemisphere.

---
Eulerian
Eulerian Research Models Solve Mass Balance Equation
in 3-D Assemblage of Grid Boxes
The mass balance equation is the finite-difference approximation of the continuity equation.
Solve Continuity Equation for Individual Grid Boxes
Models can presently afford ~ 106 grid boxes
In global models, this implies a horizontal resolution of 100-500 km in horizontal and ~ 1 km in vertical
Drawbacks: “numerical diffusion”, computational expense
Courtesy of Daniel J. Jacob

---
Lagrangian
In Eulerian Approach, Describing the Evolution of a Pollution Plume Requires a Large Number of Grid Boxes
A Lagrangian “puff”
Model offers a much
simpler alternative
Courtesy of
Daniel J. Jacob
Fire plumes over southern California on 25 October 2003.

---
Puff
Puff Model: Follow Air Parcel Moving with Wind
CX(x, t)
In the moving puff,
wind
…no transport terms! (they’re implicit in the trajectory)
CX(xo, to)
Application to the chemical evolution of an isolated pollution plume:
CX,b
CX
In pollution
plume,
Courtesy of
Daniel J. Jacob
Kdilution (s-1) is the dilution rate constant
Also called entrainment rate constant

---
Column
Column Model for Transport Across Urban Airshed
Temperature Inversion
(defines “mixing depth”)
Emission E
In column moving across city,
CX
Courtesy of Daniel J. Jacob
x
0
L

---
Lagrangian Research
Lagrangian Models Follow Large Number of “Puffs”
Individual puff trajectories over time t.
C(x, tot
Advantages of Puff models over Eulerian models:
Computational performance (focus puffs on region of interest).
No numerical diffusion.
Disadvantages of Puff (Lagrangian) models:
Can’t handle mixing between puffs and can’t handle nonlinear processes
Spatial coverage by puffs may be inadequate
C(x, to)
Concentration field at time t defined by n puffs
Courtesy of Daniel J. Jacob
Courtesy of Daniel J. Jacob

---
Lagrangian Receptor
Lagrangian Receptor-Oriented Modelling
Backward in Time
Run Lagrangian model backward from receptor location, with points released at receptor location only.
Efficient cost-effective quantification of source influence distribution on receptor (“footprint”)
Courtesy of Daniel J. Jacob