Terminal
Errors and Uncertainty
A value without uncertainty contains no information!
i
As far as the laws of mathematics refer to reality, they are not certain; and as far as they are certain, they do not refer to reality." (Albert Einstein)
"In this world, nothing is certain but death and taxes." (Benjamin Franklin)
"As complexity rises, precise statements lose meaning, and meaningful statements lose precision." (Lotfi Zadeh)
"The whole problem with the world is that fools and fanatics are always so certain of themselves, with wiser people so full of doubts." (Bertrand Russell)
"We demand rigidly defined areas of doubt and uncertainty." (Vroomfondel - in "The Hitchhiker's Guide to the Galaxy" by Douglas Adams)

---
Error
Sources of Error
Static
Errors that are present when the input is constant.
Dynamic
Errors that are present when the input changes.
Drift
Errors that result from sensor changes with time.
Exposure
Errors due to imperfect
coupling between the
sensor and what is
measured.

---
Errors
Definition of Errors
The term error represents the imprecision and inaccuracy of a measurement or numerical computation.
%epsilon_"abs" = abs (tilde %chi - %chi)
Absolute Error – The magnitude of the different in the approximation ( ) and the true value (χ).
tilde %chi
%epsilon_"rel" = abs (tilde %chi - %chi)OVER abs %chi
Relative Error – The absolute error normalized (relative) to the true value.

---
Systematic Errors
Random and Systematic
 Errors
Measurement uncertainty is due to random and systematic errors.
Random errors are statistical fluctuations in the measured data due to the precision limitations of the measurement device.
Random errors usually result from the experimenter's inability to take the same measurement in exactly the same way.
Systematic errors are reproducible inaccuracies that are consistently in the same direction.
Systematic errors are often due to a problem which persists throughout the entire experiment.
Mistakes made in calculations, in reading values, and in using instruments are not considered in error analysis.
Typically, it is assumed that the experimenters are careful and competent; however, some experimenters are more careful than others so it is important to know the experimenters.

---
Accuracy and Precision
Measurements and calculations can be characterized with regard to their accuracy and precision.
Accuracy refers to how closely a value agrees with the true value.
Precision refers to how closely values agree with each other.
What does this indicate about repeatability?
[Speaker Notes: Measurements and calculations can be characterized with regard to their accuracy and precision. Accuracy refers to how closely a value agrees with the true value. Precision refers to how closely values agree with each other. The following figures illustrate the different between accuracy and precision. In the first figure, the given values (black dots) are more accurate; whereas in the second figure, the given values are more precise. The term ''error'' represents the imprecision and inaccuracy of a numerical computation.]

---
Voltage Measurements (25 Hz)
29 SEP 2005
2 SEP 2012
Time series (25 Hz) of voltage from the side slip pressure transducer on the North Dakota Citation Research Aircraft during research flights. The same data system and analog-to-digital board is used on both flights.
[Speaker Notes: Measurements and calculations can be characterized with regard to their accuracy and precision. Accuracy refers to how closely a value agrees with the true value. Precision refers to how closely values agree with each other. The following figures illustrate the different between accuracy and precision. In the first figure, the given values (black dots) are more accurate; whereas in the second figure, the given values are more precise. The term ''error'' represents the imprecision and inaccuracy of a numerical computation.]

---
Statistical Uncertainty
Uncertainty Improvements
To improve our certainty in a measurement, we can make repeated measurement.
1 Hz (25 Points)
10 sec (250 Points)
Time series with different averaging of side slip pressure transducer voltage on the North Dakota Citation Research Aircraft during 2 September 2012 research flights.

---
Uncertainty Improvements
Repeated measurements can be represented as a Histogram that represents how the measurements are distributed.

---
Statistical Characterization
What single number best characterizes the complete group of measurements?
Mode – The value(s) the come up most often.
Median – The value where 50% of the measurements are above the value and 50% below.
Mean – Sum of all measurement divided by number of measurements.
What single number best characterizes the Span, Spread and Symmetry?
Statistics of side slip pressure transducer voltage during 2 September 2012 Citation research flight (15:30-17:10 UTC).

---
Indicating Uncertainty
Instrument Calibration
Instruments are calibrated,
not data or data sets.
Provides the uncertainty by comparing instrument performance with a know standard, which is used for processing and data analysis.
Instrument Performance
Confirm Instrument is working as expected.
Significant Figures
All but the last number is certain.
The last number is uncertain.
What is the range of 20.8 0C?

---
Uncertainty
Calculated Quantities Uncertainty
A single measurement rarely gives the information desired.
Calculated quantities may contain several measurement each with an uncertainty and it is the uncertainty in the calculated quantities we are interested in.
We could assume the errors in the measured quantities combine in such a way as to drive the value of calculated quantity as far as possible from the central value.
It is more probable for the uncertainties in the basic measurement to combine in a less extreme matter so the calculated quantity error would be a probable uncertainty.
Total Temp. + TAS → Air Temp.

---
Uncertain and Agreement
When do two measurements (M) agree?
When do two measurements (M) agree within one standard deviation of uncertain?
M1
M2
M3
M4
Air Temperature [°C]

---
Single Variable
Uncertainty in Function
of a Single Variable
dz over dx = {d(f(x))} over {dx}
Z
Assume a function:
z=f(x)
%delta z = {d(f(x))} over {dx} %delta x
δZ
Z0
+- %delta x
δX
- Uncertainty in x
+- %delta z
- Uncertainty in z
Xo
X1
X

---
Two Variables
Uncertainty in Function
of Two Variables
Assume a function:
Z = f(x,y)
The appropriate quantity for calculating δz is the
dz = { partial f } over { partial x } dx + { partial f } over { partial y} dy
Total Differential:
Treat the differential as a finite difference δz that is calculated from the uncertainties in δx and δy.
%delta z = { partial f } over { partial x } %delta x + { partial f} over { partial y } %delta y

---
Breadth
Breadth of Distributions
How reliable is it to use a single number to represent the whole distribution?
The quantity that is almost universally used to measure the breadth of the distribution is the “standard deviation”.
The “best estimate” of the universe standard deviation is given by:
bar %chi
- Arithmetic Average or Mean
- Value of an Observation
- number of Observations
S = sqrt {SUM (bar %chi - %chi_i) ^ 2 over {N-1}}
%chi_i
N

---
Equation 1
Standard Deviation of Calculated Quantities
Z = f(x,y)
Assume a function:
S_z = sqrt {SUM (%delta z) ^ 2 over {N}}
Standard Deviation for the N different z values:
%delta z = { partial z } over { partial x } %delta x + { partial z} over { partial y } %delta y
Finite Difference δz is:
Z
z=f(x)
δZ
S_z = sqrt {SUM (%delta z) ^ 2 over {N}}
Z0
δX
Xo
X1
X

---
Equation 2
Standard Deviation of
 Calculated Quantities
S_z^2 = 1 over N SUM ( {partial z} over {partial x} %delta x + { partial z } over { partial y} %delta y) ^ 2
Gives:
S_z^2 = 1 over N SUM ( {({partial z} over {partial x})}^2 ( %delta x ) ^ 2 + ( { partial z } over { partial y} ) ^ 2 ( %delta y) ^ 2 + 2 {partial z} Over {partial x} {partial z} Over {partial y} partial x partial y)
S_z^2 = {({partial z} over {partial x})}^2 1 over N SUM ( %delta x ) ^ 2 + ( { partial z } over { partial y} ) ^ 2 1 over N SUM ( %delta y) ^ 2 + 2 over N {partial z} Over {partial x} {partial z} Over {partial y} SUM ( %delta x %delta y )
S_y^2 = 1 over N SUM ( %delta y ) ^ 2
S_x^2 = 1 over N SUM ( %delta x ) ^ 2
SUM ( %delta x %delta y ) = 0
S_z^2 = {({partial z} over {partial x})}^2 1 over N SUM ( %delta x ) ^ 2 + ( { partial z } over { partial y} ) ^ 2 1 over N SUM ( %delta y) ^ 2 + 2 over N {partial z} Over {partial x} {partial z} Over {partial y} SUM ( %delta x %delta y )

---
Equation 3
Standard Deviation of
 Calculated Quantities
S_z = SQRT { ( { partial z } over {partial x} ) ^ 2 S_x^2 + ( { partial z } over { partial y } ) ^2 S_y^2 }
Gives:
How Quickly Functions Changes
Spread of the Uncertainty
If z is a function of more than two variables, the equation is extended by adding similar terms.

---
Background
Reference Material
Chapter 2 and 3 of Experimentation: An Introduction to Measurement Theory and Experiment Design by D. C. Baird.