Airborne Measurements
Liquid Water Content

---
Liquid Water Content (LWC)
Basic Cloud Parameter
Icing Studies
Precipitation Potential
Comparison with Remote Sensing Measurements
Compare Measurements using Different Techniques
Hotwire Boom
WCM
RICE-B
CDP
King Probe

---
Liquid Water Content (LWC) Calculation
The amount of liquid water in a given volume of air is determined through mass integration of the cloud droplet distribution.
size 12{ ital "LWC"= ( %pi over 6 ) ρ rSub { size 8{w} } Sum cSub { size 8{i=1} } cSup { size 8{m}} {N rSub { size 8{i} }} d rSub { size 8{i} } rSup { size 8{3} } }
ρw – Density of Water
Ni – Concentration of Droplets in Size Channel i
di – Droplet Diameter in Size Channel i
m – Total Number of Channels

---
King Hotwire Probe
DMT Hotwire Probe

---
Hot Wire Probe Equations
M – Liquid Water Content (LWC)
P – Power
ρ – Density of Air
v – True Air Speed
l – Wire Length
d – Wire Diameter
Lv – Latent Heat of Vaporization
Cw– Specific Heat of Liquid Water
Ts – Temperature of Sensor Wire
Tv – Sensor Water Vaporization
Ta – Air Temperature
 C, x, a – Calibration Constants
P_Measured = P_Dry + P_Wet
P_Dry = C(T_s - T_a) * (%rho v)^x + a
P_Wet = Mldv[L_v + c_w(T_v - T_a)]
M approx (P_measured-C(T_s - T_a) * (pv)^x) over (ldv*[L_v + c_w(T_v -T_a)]) + a

---
Hot Wire Probe Calibration: 2008/07/09 Flight
2.0
King Probe Constants:
c = 2.127 * 10-5
x = 0.345
a = 5.317
Start Time = 76300
End Time = 76550
1.5
1.0
0.5
Pressure – 843 mbars
Temperature 13.9 °C
0.0
40
60
80
100
120
Air Speed * Density [kg/(m2*s)]
King Voltage [volts]

---
POLCAST2 Field Project: Summer 2008
2.0
Slope = 0.86
1.5
1.0
0.5
0.0
0.0
0.5
1.0
1.5
FSSP Liquid Water Content [g/m3]
DMT Hot Wire Liquid Water Content [g/m3]

---
0.50
King Probe - 0.218 ± 0.096
FSSP - 0.203 ± 0.085
0.45
0.40
0.35
0.30
0.25
0.20
0.15
0.10
0.05
0.00
81600
81650
81700
81750
81800
81850
81900
81950
82000
Time [sfm-UTC]
The 4 Hz averaged FSSP (Black line) and King Probe (Red Line) cloud liquid water content data for March 10, 2004 Citation flight.
Liquid Water Content [g/m3]

---
March 10, 2004 Citation Flight
3.0
Average = 0.96
stdev = 0.18
2.5
2.0
1.5
1.0
0.5
0.0
81600
81650
81700
81750
81800
81850
81900
81950
8200
Time [sfm-UTC]
FSSP/King LWC Ratio

---
0.80
FSSP – 0.077 ± 0.149
King Probe - 0.065 ± 0.123
0.70
0.60
0.50
0.40
0.30
0.20
0.10
0.00
Time [sfm-UTC]
63480
63530
63580
63630
63680
The 4 Hz averaged FSSP (Black line) and King Probe (Red Line) cloud liquid water content data for September 24, 2004 Citation Flight.
Liquid Water Content [g/m3]

---
September 24, 2004 Citation Flight

---
March 14, 2004 Flight
0.06
— FSSP
— King Probe
0.05
0.04
0.03
0.02
0.01
0.00
65100
65100
65200
65300
65400
65500
65600
65700
Time [sfm-UTC]
Ice Contamination of the FSSP LWC calculations assume spherical water droplets.
Liquid Water Content [g/m3]

---
July 20, 2010 Flight: Low Liquid Water Content
0.4
— FSSP
— Hot Wire
0.3
0.2
0.1
0.0
83090
83100
83110
83120
83130
83140
83150
Time [sfm-UTC]
Liquid Water Content [g/m3]

---
July 20, 2010 Flight: High Liquid Water Content
2.0
1.5
1.0
- King Hot Wire Probe
- Cloud Droplet Probe
0.5
0.0
83720
83730
83740
83750
83760
Time [sfm-UTC]
Liquid Water Content [g/m3]

---
POLCAST3 Field Project: Summer 2010
3.0
* July 13, 2010
* July 15, 2010
* July 20, 2010
2.5
2.0
1.5
1.0
0.5
0.0
0.0
0.5
1.0
1.5
2.0
2.5
3.0
Hot Wire Probe Liquid Water Content [g/m3]
Cloud Droplet Probe Liquid Water Content [g/m3]

---
CDP Number Concentration Spectrum: July 15, 2010
50
40
Number Concentration
- 100 to 150
- 150 to 200
- 200 to 250
30
20
10
0
0
10
20
30
40
50
Cloud Droplet Diameter [µm]
dN [#/cm3]

---
CDP Normalized Concentration Spectrum: July 15, 2010
25
Number Concentration
- 100 to 150
- 150 to 200
- 200 to 250
20
15
10
5
0
0
10
20
30
40
50
Cloud Droplet Diameter [µm]
dN/dD [#/(cm3 µm)]

---
July 8, 2010 Flight
- King Hot Wire LWC - Cloud Droplet Probe LWC - Cloud Droplet Probe Conc.
Temperature = 7 oC
0.4
60
0.3
40
0.2
20
0.1
0.0
0
84200
84202
84204
84206
84208
Time [sfm-UTC]
Droplet Concentration [#/cm3]
(Invalid – Optical Mask Issue)
Liquid Water Content [g/m3]

---
July 8, 2010 Flight: CDP Spectrum (84198-84209 smf)
5
4
3
2
1
0
0
5
10
15
20
Cloud Droplet Diameter [µm]
dN/dD [#/(cm3 µm)]

---
Conclusions
The FSSP liquid water content agrees with the King Probe LWC in ice free conditions. Cases from two different field programs found FSSP to King ratios of 0.96 and 1.20.
The cloud droplet probe uses different optical system. The July 20 POLCAST3 flights show CDP Liquid Water Content measurements 20% low compared to King Hot Wire probe measurements; however, other flights are worst.

---
     Any Questions?
[Speaker Notes: Lecture prepared by David Delene for UND physical met. class Spring 2003. Picture include aerosol balloon package launch in Feb. 1998. The University of Wyoming balloon-borne CCN Counter. The other images are from TSI, A 3010 CPC, 3025 ultrafine counter, and a 3080 Electrostatic Classifiers (www.tsi.com).]