## Slide 1
Particle Habit Imaging and Polar Scattering (PHIPS) Probe
PHIPS Probe
North Dakota
Citation Research Aircraft
16,385
Measure the angular light scattering function of individual cloud particles that are identifiable as belonging to a particular habit.
  Improved remote sensing observations.
Obtain high resolution stereo-graphic images with sufficient detail to improve understanding of riming and aggregation processes.
  Improved cloud micro-physical modeling.
Provide reliable phase identification on small and intermediate sized cloud particles.
  Improved understanding of precipitation.
Notes: Image showing the PHIPS probe in the outside PMS can on the left wing for the CapeEx19 field project to sample Florida cirrus cloud anvils in the summer of 2019. These two slide summarize the three main features of the PHIPS probe (highlighted in red) and the corresponding scientific motivations for these features.

## Slide 2
Measurements and Observations of the PHIPS Probe
16,385
Angular Light
Scattering Function
Stereo-graphic Images
Phase Identification
2019/07/26 #5,134
Averaged angular scattering functions from different campaigns, which was used to validate the MODIS C6 ice optical model (Järvinen et al., 2018).
Stereo image pairs obtained within Cirrus cloud anvils over Florida.
Stereo image pairs of a droplet (a) and a quasi-spherical ice particle (b), and the corresponding angular scattering function (c) (Waitz et al., AMT in preparation).
a)
200 µm
b)
Scattering Intensity [cts]
Scattering Angle
Angle
Normalized Angular Scattering Function
101
0
20
60
40
80
100
120
140
160
180
102
103
104
SOCRATES, RF02, #96, Droplet
SOCRATES, RF02, #613, Spherical Ice
Mie Calculation for D = 200 mu (a.u)
2019/07/25 #4,434
Notes: Examples of the three important measurements of the PHIPS Probe. Note that researchers are actively using the PHIPS probe observations to produce important scientific publications. The provided stereo-graphic images from the CapeEx19 field project illustrates the details that can be seen in the crystal aggregates. The top images pair (#5,134) is obtained at 19:51:15 UTC at an altitude 10.7 km and temperature of -33.4 °C. The bottom image pair (#4,434) is obtained at 18:53:54 UTC at an altitude of 9.6 km and temperature of -32.3 °C. While high resolution images provide an indication if spherical particles are water or ice, the difference in light scattering between 80-120 degrees clearly demonstrates the phase of the particle.